## Slide 1
Real-time scheduling, sharing resources
Adam Hoover

## Slide 2
Outline
Problems of resource sharing
Basic priority inheritance protocol
Priority ceiling protocol
Highest locker protocol

## Slide 3
Resource sharing
Time slicing processes requires careful management of resource access
word
processor
web
browser
operating system
process
process
run
resource

## Slide 4
Resource locks
critical
code
(section)
program #1
…
….
start using printer
….
end using printer
….
….
program #2
…
….
start using printer
….
end using printer
….
….
critical
code
(section)
semaphore
mechanisms like semaphores provide mutual exclusion access (mutex)

## Slide 5
Deadlock
tasks waiting on resources being used by other tasks in circular pattern
task A
time
allocates R1
task B
preempts
allocates R2
attempts to allocate R1
attempts to allocate R2
higher
priority

## Slide 6
Priority inversion
priority inversion = higher priority task waiting on lower priority task
we seek to limit the maximum blocking time
task A
time
allocates R1
task B
preempts
attempts to
allocate R1
R1 is freed
higher
priority
task C
preempts
blocking time
terminates
still owns R1
allocates R1

## Slide 7
Basic priority inheritance
If a task requests an unavailable resource, currently in use by a lower priority task,
then the lower priority task temporarily inherits the higher priority of the waiting task
dynamic priorities = task priorities can be altered by scheduler (O/S)
Imagine being able to increase speed of slower car remotely...

## Slide 8
Basic priority inheritance
task A gets temporary priority boost, reducing blocking time
task A
allocates R1
task B
preempts
attempts to
allocate R1
R1 is freed
prio(A) reset
higher
priority
task C
preempts
blocking
time
terminates
prio(A)=prio(C)
allocates R1
terminates

## Slide 9
Transitive inheritance
priority inheritances can cascade, extending blocking time
task A
allocates R1
task B
attempts to
allocate R2
R1 is freed
prio(A) reset
higher
priority
task C
preempts
blocking time
terminates
prio(A)=prio(B)=prio(C)
allocates R2
terminates
preempts
allocates R2
prio(B)=prio(C)
attempts to
allocate R1
allocates R1
R2 is freed
prio(B) reset

## Slide 10
Priority ceiling protocol
Each resource has a ceiling priority = highest priority of any task that uses it.
System ceiling = highest ceiling priority of any resource currently in use.
On any resource request, the task must either:
have a priority > current system ceiling, or
own the resource setting the current system ceiling
If request denied, blocking task temporarily inherits priority of requesting task
task | priority | resources used
A | P1 | R1
B | P2 | R1, R2
C | P3 | R2
higher
priority
resource | ceiling priority
R1 | P2
R2 | P3

## Slide 11
0
P3
Priority ceiling protocol example
priority requests checked against ceiling protocol tests
task A
allocates R1
task B
allocates R2
R1 is freed, prio(A) reset
higher
priority
task C
preempts
terminates
prio(A)=prio(B)
R2 freed
terminates
preempts
attempts to
allocate R2
R1 freed
preempts,
allocates R2
allocates R1
system
ceiling
0
P2
P3
P2
0
R2 freed

## Slide 12
Highest locker protocol
Each resource has a ceiling priority = highest priority of any task that uses it.
System ceiling = highest ceiling priority of any resource currently in use.
On any resource request, the task must either:
have a priority > current system ceiling, or
own the resource setting the current system ceiling
If request denied, blocking task temporarily inherits priority of requesting task
If granted, requesting task temporarily inherits the resource’s ceiling priority + 1
task | priority | resources used
A | P1 | R1
B | P2 | R1, R2
C | P3 | R2
higher
priority
resource | ceiling priority
R1 | P2
R2 | P3

## Slide 13
Highest locker protocol example
acquired resources cause immediate priority changes
task A
allocates R1
task B
allocates R2,
prio(C)=P3+1
R1 is freed, prio(A) reset
higher
priority
task C
preempts
terminates
prio(A)=P2+1
R2 freed,
prio(C) reset
terminates
cannot
preempt
R1 freed
allocates R2,
prio(B)=P3+1
allocates R1
system
ceiling
0
P2
P3
P2
P3
0
R2 freed
prio(B) reset
preempts
0

## Slide 14
Ceiling/locker protocols
Both eliminate deadlocks
Both reduce maximum blocking time
Each task can only be blocked once per resource
Locker protocol changes priorities more often but has fewer task switches
A set of tasks is schedulable if:
i=1…n
let k=1…i
let l=1…
for some (k,l)
max blocking

## Slide 15
How to see priorities (linux)
ahoover@apollo01> ps -e -o uid,pid,ppid,pri,ni,cmd | more
UID PID PPID PRI NI CMD
0 1 0 19 0 /sbin/init
0 2 0 19 0 [kthreadd]
0 9 2 139 - [migration/0]
0 47 2 39 -20 [netns]
0 49 2 19 0 [khungtaskd]
0 50 2 39 -20 [writeback]
0 51 2 14 5 [ksmd]
0 52 2 0 19 [khugepaged]
...
priority
niceness
linux priorities are combinations of (a) user vs system tasks, (b) scheduler used, and (c) niceness levels used to make adjustments within a small range
‘nice’ and ‘renice’ commands can be used to adjust priorities at startup and during execution, respectively

## Slide 16
How to see priorities (windows)
priority
niceness
CTRL-ALT-DEL ….. Start task manager
…right-click task